## Slide 1: Benefits and properties of scratchClient
Makes the connection between Scratch and
  External hardware connected to the Raspberry Pi GPIO I/O pins
  External hardware connected to the GPIO pins of an Arduino Uno or Nano
    Arduino is connected to Raspberry Pi via USB
  Other software services, like SonicPi or sending messages via Twitter
Children can control the external hardware by using comprehensible names.
  So e.g. BigRedLED rather than GPIOpin5

## Slide 2: Benefits of using an Arduino for connecting external hardware
Arduino has
  analog in
  a hardware pulsewidth modulaton (PWM) for more stable servo control.
Arduino uses 5 volt. Raspberry Pi GPIO pins are not 5 volt tolerant.
If children mess up with electronics, they potentially blow up an Arduino of 2 euro rather than a Raspberry Pi of 35 euro.
Keeping the setup transportable, now only one USB plug has to be connected, rather than otherwise a large pin header.