## Slide 1: Physical computing from Scratch using scratchClient – Beginners Control servos, LEDs and more from Scratch using RPi, Arduino, scratchClient
Hans de Jong & Gerhard Hepp
Pi And More 10 1/2
Stuttgart – 24 February 2018

## Slide 2: Part 1: Introduction

## Slide 3: Changes since the workshop
scratchClient has been adapted
It now has two modes of representing the blocks:
  Workshop mode: use name value pairs
  Verbose mode: every input or output variable has its own block
In the workshop we used the workshop mode, therefore we use that also in this presentation
The setting of those modes and getting the blocks in the project has changed somewhat and that has been adapted in these slides.

## Slide 4: Workshop organisation
Welcome and introduction presentation (5 min).
After that everyone will work at his or her own pace.
Choose with your “workplace partner” which topics you want to do.
  There is more material than what can be covered in 110 minutes.
Language: Both German and English
At the end copy the material you created to your USB stick (if you want)
Break down & clean up (5 min)
The major steps:
  Get a working hardware and scratchClient config using a scratchClient config tool.
  Put components on the board and test out your setup.
  Write some code in Scratch
  Add more hardware and update the config file.
  And repeat this.

## Slide 5: Objectives
At the end of today you should be able to do a few of these items:
  Reproduce the setup at home (provided you have the hardware  )
    You can get all files via https://github.com/hansdejongehv/scratchClient-Tutorials
    Or go to www.github.com and search for scratchClient
  Understand (depending on how far you get and how deep you dive in)
    Digital output (e.g. lighting a LED)
    Digital input (e.g. sensing a button)
    Analog input (e.g. from a potentiometer)
    Pulse Width Modulation (PWM)
      For dimming LEDs
      For controlling servos
      For sounding a buzzer
  Understand what all the resistors are for
  Be able to configure and run scratchClient
  Program Scratch to control the physical input and output
  Monitoring the inputs and outputs
Have fun!

## Slide 6: Non-objective
It is not an objective to create a complete useful game or other program.
  You can do that with your own creativity at home now that you know how to control several pieces of hardware from Scratch using scratchClient.

## Slide 7: Example of what can be created with Scratch and scratchClient
https://www.youtube.com/watch?v=Qo1gnXNzhqE

## Slide 8: Versions of Scratch
scratchClient can work with
  Scratch 1.4
  The (for Raspberry Pi) new Scratch 2
This workshop is written for Scratch 2
  Scratch 2 on Raspberry Pi has some bugs, but we will work around it.
  If you want to see how to do it for Scratch 1.4, see the end of the presentation in Appendix A.

## Slide 9: Only a few rules today
Always put a resistor in series with the components when indicated.
  If you think there is no need then please tell us and we will explain what the reason is.
When changing the wiring
  Detach the USB cable from the Arduino Nano
  Switch off the 9V power
  Check, double check and check again whether the wiring is correct. You may blow up components when wiring wrongly!
  Make sure that you both (4 eyes principle) are convinced the wiring is OK before reconnecting and turning on power again.
  After changing a config file: restart scratchClient
If something breaks down or gets damaged: we have some spare material
  Do not put anything that is broken back into the box please.

## Slide 10: De opzet
Arduino Nano
Raspberry Pi 3B
Scratch 2 run time
scratchClient
scratchClient Schets
scratchClient Config file
Programma in Scratch
Definieert de functies van de GPIO pennen op de Arduino (en de RPi) en geeft ze logische namen.
Voorgedefinieerde sprites (met code, geluid en uiterlijken)
Standard setup
Geprogrammeerd door de leerlingen
Voorbereid door de leraar, ouder of ervaren leerling.
Scratch 2 extentie voor scratchClient

## Slide 11: Often asked: why using an Arduino?
Question: why not just the GPIO pins of the Raspberry Pi?
Arduino has analog in and has a hardware pulsewidth modulaton (PWM) for more stable servo control.
Arduino uses 5 volt. Raspberry Pi GPIO pins are not 5 volt tolerant.
If children mess up with electronics, they potentially blow up an Arduino of 2 euro rather than a Raspberry Pi of 35 euro.
Keeping the setup transportable, now only one USB plug has to be connected, rather than otherwise a large pin header.

## Slide 12: Choose what you want to do
Workshop is for everyone, from beginners to experts.
Not enough time to do all, so choose what you want to do.
Yellow slides have background information and you can skip them if you want or look at it later
Recommended
  All: learn to configure scratchClient by doing LEDs (digital out) and Button (digital in)
  All: try it out in Scratch
  After that: select further topics from separate files
    Intermediate level
    Advanced level
    Expert level

## Slide 13: Part 2: Getting to know the components

## Slide 14: Breadboard
Used to quickly build electronic circuits
Note the 2 rails for + (VCC) and – (GND)
Note on every column (vertical) the 2 bars with 5 interconnected holes each.

## Slide 15: De Arduino Nano en het adapterbord
Voedingsaansluiting 9-12 volt
Arduino Nano met 328P processor
Micro USB poort
Per GPIO signaal 3 pennen:
S (blauw = signaal)
V (rood = VCC = +)
G (zwart = GND = -)
(heel handig om b.v. servo’s aan te sluiten)
Digitale poorten
Analog poorten (de meeste ook bruikbaar als digitale poorten)
Reset knop
Reset knop

## Slide 16: What the final board looks like …
… at the end of the basic level
Other picture to be made

## Slide 17: … at the end of the intermediate level …

## Slide 18: … and at the end of the advanced level

## Slide 19: Part 3: Loading the sketch in the Arduino (in the workshop: optional, at home: mandatory)

## Slide 20: Preparing for programming the Arduino Nano
The Arduino needs to run a program (in Arduino terms: sketch) so that it can communicate with the Raspberry Pi and understand the messages from scratchClient.
We need to start putting that in.
  However in the workshop that has already been done, so you can skip the next slide, unless you want to try for yourself.
  If you are doing this at home, then you will need to do it however.

## Slide 21: Uploading scratchClient to the Arduino
Navigate to the scratchClient sketch for Arduino Uno in /home/pi/scratchClient/arduino/arduinoUno
Double click to open the Arduino IDE
Click Tools and make sure that these are set:
  Board: Arduino Nano
  Processor Atmega328
  Port: the port where the Arduino Nano is connected (normally /dev/ttyUSB0)
Click on the Upload button.
Wait till the completion of the Upload is reported (without errors).

## Slide 22: Part 4: Defining the configuration
Give names to pins and define the purpose of the pin

## Slide 23: Starting the config tool
We have put an empty config file on the desktop:
  scratchClient-Tutorial.scl
Right click the file and choose scratchClient Edit

## Slide 24: Define the first config file
Double click a cell to get a drop down menu
  First for direction then for function.
Make sure to give all pins a name if you choose something else than void in direction.
  So make sure not to save if you still have red borders around cells. scratchClient will fail to start with such a config file.
The tool checks wrong configurations. Examples:
  Pins 0, 1 and 13 cannot be used at all
  Analog In only available on A0 to A7
  Pins A6 and A7 can only be used for Analog In
  Pins 9 and 10 cannot be used for PWM if any pin is configured for servo (see later)
D4
Direction: out
Function: output
scratchName: BigRedLED
D7
Direction: in
Function: input_pullup
scratchName: Button
Parameter serial.device: /dev/ttyUSB0

## Slide 25: Save the config file
Save the file (ctrl-S or File  Save).
Warning: closing the file without saving will loose all changes.
Leave the tool open for the next exercises.

## Slide 26: Part 5: Wiring the board and run the first setup

## Slide 27: Put the board in front of you in this way

## Slide 28: Use short wires and use the indicated holes
There are some short wires (10 cm) and some longer (15 cm)
Use the shortest that you can
  Get a less messy setup
  You may otherwise run out of long wires later
Ignore wire colors.
You can in principle build up at different places on the breadboard, however …
  … please use the indicated columns to avoid running out of space on the breadboard in the later part of the workshop.

## Slide 29: Connect the power wires

## Slide 30: Plaats de rode LED en de knop
Lange draad = plus (+) kant
Korte draad = min (-) kant
Naar pen 7
Naar pen 4
Notes: The LED has polarity. The long wire is the + side, the short wire is minus. You must connect LEDs such that the minus side of the LED is closest to the minus on the board and the plus side is of the LED is closest to the plus on the board – which is for this LED provided by the Arduino pin.

## Slide 31: Why putting a resistor in series with the LED?
Arduino
+5 Volt
0 Volt
180 Ohm resistor (the thick ones in the box)
Digital output
This resistor is for limiting the current through the diode
(you will blow up the LED and/or the Arduino otherwise)
The LED
+
-

## Slide 32: What does Arduino need on a Digital Input pin?
A digital input pin of Arduino needs to get either
  0 volt input (actually, 0 to 1.5 volt is considered a LOW input signal)
  5 volt input (actually, 2.5 volt to 5 volt is considered a HIGH input signal)
If it gets something between 1.5 volt and 2.5 volt, the interpretation will not be stable (could be LOW or HIGH).
If it does not get any signal in, then the interpretation of the signal is not stable (could be LOW or HIGH).

## Slide 33: Producing a LOW value
Arduino
+5 Volt
0 Volt
Digital input
If the button is closed, the digital input signal is set to 0 volt which is detected as LOW.
The button
33
But what will the Arduino detect if the button is open?

## Slide 34: Producing a HIGH value
Arduino
+5 Volt
0 Volt
30
kOhm
Digital input
If the button is pressed, then it connects the input of the Arduino to 0 volt. There will run a small current through the resistor, but the input will be 0 volt.
If the button is open, the resistor will pull up the input to 5 volt. A very small current will flow through the resistor, but is small enough that the voltage on the digital input will be very close to 5 volt = HIGH.
This is a pull-up resistor that provides 5 Volt if the button is opened
34

## Slide 35: Producing a HIGH value without external resistor
Arduino
+5 Volt
0 Volt
30 kOhm
Digital input
You do however not have to connect the resistor externally. It can be configured in the Arduino itself by specifying input_pullup rather than input.
35

## Slide 36: Danger when misconfiguring
Arduino
+5 Volt
0 Volt
30 kOhm
Digital input
This works fine, but what happens if you misconfigure the pin to be Digital Output, the value set to HIGH and the button is pressed?
If the Arduino makes the pin HIGH (5 volt) and the button connects to LOW (0 volt)  short circuit and the Arduino will be blown up.
36

## Slide 37: Resistor in series to prevent damage in case of misconfiguration
Arduino
+5 Volt
0 Volt
30 kOhm
Digital input
Therefore always include a 1 kOhm resistor in series with the switch.
If misconfigured, there will run a small current through the resistor rather than causing a short circuit.
The input will be 1 kOhm / (30 kOhm + 1 kOhm) * 5 volt = 0,15 volt.
See appendix B for more info.
37
1 kOhm

## Slide 38: Check / double check
Please now check both of you that the wiring is correct.

## Slide 39: Bringing things together
Connect the 9 Volt connector to the board and switch power on
  Although as long as you are only having a LED that is used, the power supplied via USB is sufficient
Connect the USB connector to the Arduino
Doubleclick scratchClient Tutorial.scl on the desktop to start scratchClient with the config file you have just updated
It will also open a browser window where you can see variables
  Explained later in the presentation
In the terminal window you will see complaints that scratchClient has no connection to Scratch
  Which is logical because Scratch was not started yet.

## Slide 40: Start Scratch 2
Simplest is to start the file on the desktop
Doubleclick the icon
See the appendix how make such a file yourself
  There are some anomalies to deal with in the current release of Scratch 2

## Slide 41
Click on this sprite to make the extension blocks visible.

## Slide 42
Clicking on the green sprite caused the extra blocks to appear

## Slide 43: Create the Scratch program
Create this program in Scratch (put it in the screen or the Cat sprite)
Try it out (click the set of blocks or click the green flag above the animation window).
Digital in (Button):
  0 = pressed
  1 = not pressed
Digital out (LED)
  0 = off
  1 = on
Analyse how the program works.
Use these arrows to select the correct value (the black on grey background is not so easily visible)

## Slide 44: Does it work? (see next slide for help)
If the LED on the Arduino is blinking slowly only then the config is downloaded and only then scratchClient works.
  It may take 10 seconds after both scratchClient and the scratchClient extensions in Scratch 2 are loaded before this happens.
  So 10 seconds after you clicked on the green sprite.

## Slide 45: You can monitor the values that are exchanged
Together with scratchClient, the browser is opened with URL localhost:8080/adapters
Note the input & output directions:
  Output of an adapter is an input for scratch
  Output of scratch is an input for the adapters.
  Hence the names input and output look to be reversed from what is in the config file.
  Therefore best refer to the variable names.
You will see that values are only displayed after they have changed (otherwise a question mark (?) is displayed).
Not for now, but you can click the field and type a value which then will be sent in the appropriate direction.

## Slide 46: Change the program
Make a change in the program so that the LED goes on when the button is pressed.
There are (at least) two ways
You need the blocks depicted here
Blocks for method 1
Blocks for method 2

## Slide 47: What if it does not work?
Check whether you have multiple Scratch instances open
  scratchClient can only work with one Scratch at a time (regardless of being Scratch 1.4 or Scratch 2).
Check if the blue LED on the Arduino Nano is blinking slowly.
Sometimes, especially after reboot, if everything seems fine, disconnecting and reconnecting the Arduino Nano may help.
Try monitoring the variables, see before.

## Slide 48: One reminder …
Save your Scratch program regularly. Otherwise it will be lost on power out.
  Power out can easily happen since you are pulling cables and may impact the power connector in the Raspberry Pi.
Here come some current Scratch 2 anomalies on Raspberry Pi
  You should not use spaces in filenames (if you do, Scratch 2 cannot find the file when started up)
  Scratch 2 forgets the folder where the file was opened from (Desktop). Just save it in /home/pi as Scratch proposes
  Scratch 2 will save it with a .sbx extension regardless what you specify.
Hence once after power up
  On the desktop, doubleclick CleanUpScratchFiles.sh
  You can minimize the window, but let it run forever
  This will permanently monitor the folder /home/pi, and
    Move all files with .sbx and .sb2 to the desktop as .sb2 files
    Any spaces in filenames are removed
    If there is already such a file on the desktop, it will be moved to the folder ScratchProgramsBackup on the desktop
If you reopen a saved file, click the green sprite once again to load the extension blocks

## Slide 49: Part 6: Adding the Big Green LED

## Slide 50: Adding the green LED

## Slide 51: Check and reconnect
Check the correct wiring
Switch on the 9V power
Connect the USB cable again

## Slide 52: Update the config file and restart scratchClient
Use the config tool (which should still be open)
Define an output (direction: out, function: output) on pin 2 and call it BigGreenLED
Save the config file (and leave the tool still open)
Doubleclick scratchClient Tutorial.scl on the desktop again
This will stop the previous instance of scratchClient and restart with the updated configuration.
Remove the extension block.
  Right click here
  Choose Remove extension blocks
Add the extension block again.
  You will see in the More Blocks section that you can now choose to send values to BigGreenLED

## Slide 53: Update Scratch
Add code that does this:
  Press button: LED goes on
  Press once more: LED goes off
You need these program elements.

## Slide 54: This is the end of the beginners tutorial
You got digital out (LED) and digital in (a button) working
You know how to work with scratchClient and Scratch 2
You know how to configure scratchClient
If you want and have time you can
  Look at some of the yellow slides if you skipped them earlier
  Continue with one of the next levels
    These are in different files.
Otherwise,
  Copy the material to a USB stick and clean up. See further below.

## Slide 55: Overview of next levels
Intermediate level
  Analog In: Potentiometer
  Pulse Width Modulation (in the absence of analog out)
    Dimming a LED
    Controlling a servo
    Controlling a buzzer
Advanced level
Expert level

## Slide 56: Part 10: Take your work home

## Slide 57: Do you want to take your work home?
If you brought your own USB stick, then connect it and copy the scratchClient -Tutorial.scl file on the desktop, plus all .sb2 files that you created on the desktop
The rest of the material you can download from www.github.com, search for scratchClient-Tutorial
Take the flyer with you to remember where to find the material on github.

## Slide 58: Part 11: Summary & take aways

## Slide 59: Takeaways of the beginners workshop
Functions that a pin on Arduino can have:
  Digital In
  Digital Out
  Analog In *
  No Analog Out
  Pulse Width Modulation as alternative *
    For modulating the brightness of a LED
    For controlling a servo
    For controlling a buzzer
  There a few more, see the advanced level tutorial
  You can configure pull up resistors on Digital In
With scratchClient you define:
  Function of each pin
  Symbolic name for each configured pin
scratchClient config is the tool to setup the configuration
Restart scratchClient after you changed the configuration
Put a resistor in series with LEDs
Put a resistor in series with switches
Configure a pull up resistor if the input signal goes between 0 Volt and being open rather than between 0 Volt and 3 to 5 Volt.
In Scratch 2, you use the extension block for scratchClient to get blocks that you can use to interact with scratchClient
You can monitor the value of all pins from the browser
scratchClient can do much more…
There are some anomalies, therefore
  Save the Scratch 2 files in the home folder (as Scratch 2 proposes)
  Run CleanUpScratchFiles.sh on the desktop (once after start up)
  Use the files on the desktop
* See the intermediate level tutorial

## Slide 60: Part 12: Clean up / teardown

## Slide 61: If your scratchClient day ends here …
Unplug the board from USB and power it off
Please remove all components and wires from the breadboard
Remove all wires from the Arduino board.
Leave the wires on the 3 color LED (you did not use that)
Leave the wires on the buzzer
If something is broken, please
  Throw it away or hand it in (if it is unclear)
  Put a note in the box that it is missing
  Do not put anything that is broken back in the box
Shutdown the Raspberry Pi running
Let us know what you thought about this workshop, now orally or later by email
  hans.piam@hanselma.nl
  heppg@web.de

## Slide 62: Appendix A Extension blocks in Scratch 2

## Slide 63: How to add extension blocks
Because of some anomalies, the loading of extension blocks is somewhat tricky.
You can use the way explained earlier.
This appendix explains how to create this from scratch.
Step 1: Make sure that scratchClient is running.

## Slide 64: Step 2: Start Scratch 2

## Slide 65: Step 3: Get scratchClient blocks (1 of 2)
Click on More Blocks
Click on Add an Extension
Choose scratchClient
Now a loader for the extra blocks of scratchClient get included.
However we now need to load the real blocks …

## Slide 66: Step 4-7: Get scratchClient blocks (2 of 2)
Step 4: Drag this block to the Scripts area
Step 5: Choose here workshop
Step 6: Click the block so that the extra blocks will appear.
Step 7: See the blocks appear

## Slide 67: Saving will loose the blocks
If you reopen the file after it was saved,
  The scratchClient extension loader will have been preserved
  The real blocks have disappared
  And you will see many blocks like this
Hence after opening you need to do steps 4 – 7 again.
Alternatively, see next slide.

## Slide 68: Alternative for steps 4 – 7
Instead of doing steps 4 – 7 manually every time the file is loaded you can:
Include a sprite called Load Name-Value Extension Blocks.sprite2 from the folder ~/scratchClient-Tutorials/scratchClientExtension/Sprites
That sprite has a small green square that you can click to get the extra blocks loaded every time that you reopen a file

## Slide 69: Another representation of blocks
scratchClient blocks can also be represented with one block per input or output value
You would then get e.g.
  A separate block for BigRedLED
  A separate block for BigGreenLED
  A separate block for each input variable (here only Button)
You can get this representation by selecting verbose on the loader block

## Slide 70: Easily get the verbose version of the blocks
Include a sprite called Load Verbose Extension Blocks.sprite2 from the folder ~/scratchClient-Tutorials/scratchClientExtension/Sprites
That sprite has a small green circle that you can click to get the extra blocks loaded every time that you reopen a file.
  Contrast that with the loading of name value pairs for which you use the other sprite that has a small green rectangle.

## Slide 71: Appendix B When using Scratch 1.4

## Slide 72: The setup
Arduino Nano
Raspberry Pi
2B or 3B
Scratch 1.4 run time
scratchClient
scratchClient Sketch
scratchClient Config file
Program in Scratch
Remote Sensor Protocol Over socket 42001
Global variables
Broadcasts
Defines function of the GPIO pins on the Arduino (and RPi) and gives them logical names.
Predefined sprites (with some code, sounds and costumes)
Standard setup
Programmed by the students
Prepared by the teacher or expert

## Slide 73: Defining the config file
Nothing new, you can use the exact same config file for Scratch 1.4 as for Scratch 2.

## Slide 74: Create the Scratch program
Start Scratch  Programming  Scratch
Enable remote connections (right click on sensor value)
Create the variable BigRedLED, available to all sprites
Make the variable visible (tick the box in front)
Make the Button sensor visible
Save the file on the desktop.

## Slide 75: Program in Scratch 1.4
Make this program in scratch which will let the Red LED lite up when the button is released.
Test whether it works.

## Slide 76: Further …
You can now look at the Scratch 2 material earlier in the presentation.
Try out adding the BigGreenLED and the same blocks to process it.

## Slide 77: Appendix C Basic Electronics

## Slide 78: To be added

## Slide 79: End of the beginners workshop